## Slide 1: geophysical electromagnetics imaging the subsurface from shallow to deep
Lindsey Heagy
University of British Columbia -- Geophysical Inversion Facility

## Slide 2: some important problems
have in common: need to (non-invasively) image the subsurface

## Slide 3: geophysical experiments & physical properties
physical properties are intrinsic to a material (density, susceptibility, conductivity…)

## Slide 4: electrical conductivity / resistivity
A measure of how easily current passes through a material
σ: conductivity [S/m]
ρ: resistivity [Ωm]
ρ = 1/σ
Depends on many factors
Mineralogy
Porosity
Permeability
Nature of pore fluid

## Slide 5: electromagnetic experiments
Sources:
grounded or inductive
controlled or natural
Waveform
harmonic (FDEM)
transient (TDEM)
Survey location
airborne
ground
boreholes

## Slide 6: inductive sources: time-domain
air: 10-8 S/m
background: 10-2 S/m
layer

## Slide 7: inductive sources: time-domain
current density
db/dt

## Slide 8: inductive sources: time-domain
current density
db/dt

## Slide 9: physics: frequency domain
high frequency ~ early times, low frequency ~ later times
Jy imag
B imag
100 kHz
10 kHz
skin depth

## Slide 10: forward and inverse problems

## Slide 11: statement of the inverse problem
Given
observations:
uncertainties:
ability to forward model:
Find the Earth model that gave rise to the data

## Slide 12: statement of the inverse problem
Given
observations:
uncertainties:
ability to forward model:
Inverse problem: Find an Earth model that fits those data and a-priori information

## Slide 13
Simulation and parameter estimation in geophysics
common framework for simulations & inversions
accelerate research: build upon others work
facilitate reproducibility of results
build & deploy in python
open-source
https://simpeg.xyz

## Slide 14: Multi-scale EM geophysical methods
Controlled-source EM
Natural source EM
Depth from the surface
meters
Tens of meters
Hundreds of meters
Kilometers
Inductive
Grounded
Tens of kilometers
Hundreds of kilometers

## Slide 15: Multi-scale EM geophysical methods
Controlled-source EM
Natural source EM
Depth from the surface
meters
Tens of meters
Hundreds of meters
Kilometers
Inductive
Grounded
Magnetotellurics (MT)
Z-axis Tipper EM (ZTEM)
Tens of kilometers
Hundreds of kilometers
Airborne EM (AEM)
Ground-based EM
ERT
Towed-TEM

## Slide 16: important problems: scales and surveys

## Slide 17: permafrost: near surface, large areas
Airborne : cover large areas
Frequency-domain EM system (400Hz – 135k Hz)
(Froese et al., 2024, Moshtaghian et al., 2024)

## Slide 18: minerals, geothermal: large scales & seeing deep
natural source: rely on lightning strikes, solar wind as our source (unknown strength)
lightning
aurora
skin depth (m)

## Slide 19: minerals: intermediate scale, multiple data types
Diamond exploration: rock units identified using multiple physical properties
Devriese et al. 2017, Fournier et al. 2017, Kang et al. 2017

## Slide 20: minerals: intermediate scale, multiple data types
Petrophysically and Geologically Guided Inversion
brings in petrophysical information (GMM)
builds a quasi-geology model
important components in the inversion
  multiple data misfits
  including petrophysical information
T. Astic

## Slide 21: CO2 sequestration, hydrocarbons: fine scales & large contrasts
steel casings: highly conductive, magnetic
grounded sources: helpful for exciting & detecting deep targets

## Slide 22: unexploded ordnance: small scales
near surface (or seafloor), need to detect & classify UXO vs clutter
?
UXO
Mortar
76 mm
popcan
Not UXO

## Slide 23: case studies
groundwater
CO2 sequestration
unexploded ordnance

## Slide 24: case studies
groundwater
CO2 sequestration
unexploded ordnance

## Slide 25: groundwater in Myanmar
Improving Water Security in Mon state, Myanmar via Geophysical Capacity Building
Bring geophysical equipment to Mon state Myanmar
Train local stakeholders
Provide open-source software & educational resources

## Slide 26: groundwater in Myanmar: important components
7 step framework for case studies
Setup
Physical properties
Survey
Data
Processing
Interpretation
Synthesis
Open source software and resources
Jupyter notebook “apps” for concepts and data processing
https://courses.geosci.xyz/gwb2020

## Slide 27: groundwater in Myanmar
Phayar Ngoteto Village
In 2018: 1D inversion suggested aquifer at 30-50 m
Well drilled to ~60 m: no significant water
In 2020 (before covid...):
return and conduct a 2D survey
7 step framework
Setup
Physical properties
Survey
Data
Processing
Interpretation
Synthesis

## Slide 28: groundwater in Myanmar
Main diagnostic:
Water bearing region ~ 40-140 Ωm
7 step framework
Setup
Physical properties
Survey
Data
Processing
Interpretation
Synthesis
Hydrogeological Unit | Resistivity (Ωm)
Alluvium and laterite (dry) | 200-800
Alluvium and laterite (saturated) | 30
Sand aquifer | 50-100
Clay aquitard | 10-20
Bedrock (eg. granite) | 500-1000
Fractured/Weathered bedrock (with fresh water) | 40-400

## Slide 29: groundwater in Myanmar
Survey: 2D DC resistivity
7 step framework
Setup
Physical properties
Survey
Data
Processing
Interpretation
Synthesis
Wenner-Schlumberger
Dipole-Dipole
data plotted in pseudosections

## Slide 30: groundwater in Myanmar
Survey: 2D DC resistivity
7 step framework
Setup
Physical properties
Survey
Data
Processing
Interpretation
Synthesis
Wenner-Schlumberger
Dipole-Dipole

## Slide 31: groundwater in Myanmar
Inversion: estimate a model of the subsurface
7 step framework
Setup
Physical properties
Survey
Data
Processing
Interpretation
Synthesis

## Slide 32: groundwater in Myanmar
7 step framework
Setup
Physical properties
Survey
Data
Processing
Interpretation
Synthesis
2020 Drill Hole

## Slide 33: groundwater in Myanmar
7 step framework
Setup
Physical properties
Survey
Data
Processing
Interpretation
Synthesis
2020 Drill Hole
>1000 gph
Field surveys at 23+ villages by engineers, geoscientists in Myanmar
Acquired data, interpreted, spotted drill holes using open source software

## Slide 34: open educational resources
https://geosci.xyz
undergrads at UBC
electromagnetics course: 26 locations worldwide
Notes: 30k users for EM geosci, 25k for GPG

## Slide 35: case studies
groundwater
CO2 sequestration
unexploded ordnance

## Slide 36: an example: monitoring with steel cased wells
applications: CO2, geothermal, wastewater injection, …
steel-casing: complicates numerical simulations (highly conductive, magnetic)
but… helpful for bringing current to depth
Cylindrical mesh

## Slide 37: electromagnetics: basic equations (quasi-static)
* Solve with sources and boundary conditions
Time
Frequency
Faraday’s Law
Ampere’s Law
Constitutive
Relationships
(non-dispersive)
No Magnetic Monopoles

## Slide 38: numerical simulations in SimPEG: frequency domain EM
Continuous equations
Finite volume discretization
Eliminate b to obtain a second-order system in e
(Heagy et al., 2017)

## Slide 39: numerical simulations in SimPEG: frequency domain EM

## Slide 40: numerical simulations in SimPEG: frequency domain EM
Tensor
OcTree
Cylindrical

## Slide 41: EM experiment: no casing

## Slide 42: EM experiment with casing

## Slide 44: EM monitoring with casing
applications: CO2, geothermal, wastewater injection, settings with infrastructure…
steel-casing: complicates numerical simulations (highly conductive, magnetic)
but… helpful for bringing current to depth
Heagy & Oldenburg (2022)

## Slide 45: case studies
groundwater
CO2 sequestration
unexploded ordnance

## Slide 46: Unexploded ordnance (UXO): A global problem
Definition: a munition that was armed, fired and remains unexploded
Sources:
Regions of military conflict
Munitions and bombing ranges
Avalanche control
Countries significantly impacted by UXO

## Slide 47
Notes: Cost of clearing in canada: in $100’s millions

## Slide 48: Time-domain EM response of a UXO
UXO
not UXO
time
L1
L2 ≠ L3
L2 = L3
L1

## Slide 49: Time-domain EM response of a UXO
UXO
not UXO
time
traditional approach: use inversion to get these and then
classify by comparing L(t) with ordnance library
L1
L2 ≠ L3
L2 = L3
L1

## Slide 50: Survey and system
UltraTEMA-4 system:
4 transmitters
12 receivers (3-component)
27 time channels
Height above seabed: ~1 m
Notes: Locations accuracy: objective: 95% within 50 cm
Platform altitude: +- 0.3 m for 90%
Platform attitude: +- 5º for 90%
Blind grid for detection and classification (detect targets and reject false alarms)
1.8m x 1.8m loops
Avoid early time channels (but still able to use 150-200 microsecs)

## Slide 51: Data
Transmitter 1
Transmitter 2
Transmitter 3
Transmitter 4
UXO
Receiver 1
Receiver 12
cross-track
along-track
moving
direction
time

## Slide 52: Data
UXO
Receiver 1
Receiver 12
cross-track
along-track
moving
direction
time
Transmitter 1
Transmitter 2
Transmitter 3
Transmitter 4

## Slide 53: Data
UXO
Receiver 1
Receiver 12
cross-track
along-track
moving
direction
time
Transmitter 1
Transmitter 2
Transmitter 3
Transmitter 4

## Slide 54: Data
UXO
Receiver 1
Receiver 12
cross-track
along-track
moving
direction
time
Transmitter 1
Transmitter 2
Transmitter 3
Transmitter 4

## Slide 55: Can we classify directly from EM data?
Convolutional neural networks (CNNs)
Convolutional filters look at spatial / temporal features in the data
Training EM data for UXO classification:
Available library of ordnance objects with polarizations
Fast geophysical simulations
https://towardsdatascience.com/a-comprehensive-guide-to-convolutional-neural-networks-the-eli5-way-3bd2b1164a53
input
output

## Slide 56: Convolutional Neural Networks (CNNs)
Neural network
Supervised classification problem
provided data with labels, construct a function (network) that outputs labels given input data
predicted
true
Features
Input
Class probabilities
Image segmentation

## Slide 57: Convolutional Neural Networks (CNNs)
How do we translate these things to the UXO classification problem?
predicted
true
Input
Features
Neural network
Class probabilities
nx
nrx
J. Lopez-Alvis

## Slide 58: Defining label masks
Magnitude for each transmitter
Sum of magnitudes
Label mask
color is different
for each class
threshold
along track
position (nx)
receiver
number (nrx)
T1
T3
T2
T4
along track distance (m)
cross track distance (m)
send back to footprint
of system
For time channel #5

## Slide 59: Application to a line of data
Input features are created by using a sliding window:
cross track (m)
along track (m)
UXO

## Slide 60: Application to a line of data
Input features are created by using a sliding window:
cross track (m)
along track (m)
sliding window

## Slide 61: Application to a line of data
Input features are created by using a sliding window:
cross track (m)
along track (m)
Neural network output (class)

## Slide 62: Application to a line of data
Input features are created by using a sliding window:
cross track (m)
along track (m)

## Slide 63: Application to a line of data
Single acquisition line with three objects (classification results)
cross track
along track
Input features are created by using a sliding window:
cross track (m)
along track (m)

## Slide 64: Training dataset: dipole forward model
7 classes:
background
155 mm
105 mm
81 mm
60 mm
40 mm
clutter
# of realizations:
Training (multi-class): 400,000
Validation: 10,000
Randomly assign:
Target class
Location
Orientation
Noise level: approximate from background areas in the field data
3 m
2.5 x W
0.5 m
W - width of the system
1.5 x W

## Slide 65: Clutter design
Physics-based parameterization of EM decay:
9 parameters in total:
Estimate values for UXOs in ordnance library
Define a distance threshold
Fill the remaining space with clutter objects

## Slide 66: Field data - Sequim Bay test site (2022)
7 acquisition lines
Current workflow requires seawater response removed
Some ISOs present, we used only UXO objects to train (e.g. medium ISO ~ 81mm)

## Slide 67: Get correlated noise using a binary classifier
get spatially correlated noise from this subset of field data
object

## Slide 68: Classification map (output of CNN)

## Slide 69: Predicted labels vs truth labels - field data
predicted label
ground truth

## Slide 70: Predicted labels vs truth labels - field data
predicted label
ground truth
Discriminated clutter

## Slide 71: Predicted labels vs truth labels - field data
predicted label
ground truth
Discriminated clutter
Did not miss any UXO

## Slide 72: Predicted labels vs truth labels - field data
predicted label
ground truth
Discriminated clutter
Did not miss any UXO
Classified to closest object in training dataset

## Slide 73: UXO classification
Key points:
image-segmentation architecture
clutter design and correlated noise are important
Some limitations:
not trained to handle multiple objects in the same window
objects used to generate synthetic data should be close to the objects on the field
Future work:
explore multi-target scenario
combining with traditional approach

## Slide 74: important problems
Electrical conductivity can be a diagnostic physical property in many settings
Electromagnetic methods can be useful across a wide range of scales
Numerical tools for simulation, inversion, machine learning enable understanding of physical responses, invaluable for interpretation of data

## Slide 75: Thank you!
lheagy@eoas.ubc.ca
simpeg.xyz
geosci.xyz